## Slide 1: Chapter 3 Instructions: Language of the Machine

## Slide 2: Instructions:
Language of the Machine
More primitive than higher level languages e.g., no sophisticated control flow
Very restrictive e.g., MIPS Arithmetic Instructions
We’ll be working with the MIPS instruction set architecture
  similar to other architectures developed since the 1980's
  used by NEC, Nintendo, Silicon Graphics, Sony
Design goals: maximize performance and minimize cost, reduce design time

## Slide 3: 3.2 MIPS arithmetic
All instructions have 3 operands
Operand order is fixed (destination first) Example: C code: A = B + C MIPS code: add $s0, $s1, $s2 (associated with variables by compiler)

## Slide 4: MIPS arithmetic
Design Principle: simplicity favors regularity. Why?
Of course this complicates some things... C code: A = B + C + D; E = F - A; MIPS code: add $t0, $s1, $s2 add $s0, $t0, $s3 sub $s4, $s5, $s0
Operands must be registers, only 32 registers provided
Design Principle: smaller is faster. Why?

## Slide 5: Registers vs. Memory (3.3)
Processor
I/O
Control
Datapath
Memory
Input
Output
Arithmetic instructions operands must be registers, — only 32 registers provided (32 bits)
Compiler associates variables with registers
What about programs with lots of variables

## Slide 6: Memory Organization
Viewed as a large, single-dimension array, with an address.
A memory address is an index into the array
"Byte addressing" means that the index points to a byte of memory.
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 7: Memory Organization
Bytes are nice, but most data items use larger "words"
For MIPS, a word is 32 bits or 4 bytes.
232 bytes with byte addresses from 0 to 232-1
230 words with byte addresses 0, 4, 8, ... 232-4
Words are aligned i.e., what are the least 2 significant bits of a word address?
0
4
8
12
...
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Registers hold 32 bits of data

## Slide 8: Instructions
Load and store instructions
Example: C code: A[8] = h + A[8]; MIPS code: lw $t0, 32($s3) add $t0, $s2, $t0 sw $t0, 32($s3)
Store word has destination last
Remember arithmetic operands are registers, not memory! (isto é chamado de arquitetura “load-store”)

## Slide 9: Exemplo com array (pag. 114)
Seja g = h + A[i]; onde A é um array de 100 palavras com base apontada por $s3 e o compilador associa as variáveis g, h e i com os registradores:
  g: $s1
  h: $s2
  i: $s4
Antes de $t1  A[i] é necessário calcular o endereço do elemento (A+4*i):
    (multiply) $t1, $s4, (valor 4)
    add $t1, $s3, $t1
Agora é possível ler o endereço apontado por $t1 e executar a soma
    lw $t0, 0($t1) #temp $t0  A[i]
    add $s1, $s2, $t0, # g  h + A[i]

## Slide 10: Our First Example
Can we figure out the code?
swap(int v[], int k);
{ int temp;
temp = v[k]
v[k] = v[k+1];
v[k+1] = temp;
}
swap:
muli $2, $5, 4
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31

## Slide 11: So far we’ve learned:
MIPS — loading words but addressing bytes — arithmetic on registers only
Instruction Meaning add $s1, $s2, $s3 $s1 = $s2 + $s3 sub $s1, $s2, $s3 $s1 = $s2 – $s3 lw $s1, 100($s2) $s1 = Memory[$s2+100] sw $s1, 100($s2) Memory[$s2+100] = $s1

## Slide 12: Machine Language (3.4)
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers, $t0=8, $s1=17, $s2=18
Instruction Format (TIPO R): 000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
Can you guess what the field names stand for?
  rs: source register
  rt: target register
  rd: destination register
  op + funct: definem a instrução
Notes: Board work: Binary Numbers

## Slide 13: Machine Language
Consider the load-word and store-word instructions,
  What would the regularity principle have us do?
  New principle: Good design demands a compromise
Introduce a new type of instruction format
  I-type for data transfer instructions
  other format was R-type for register
Example: lw $t0, 32($s2) 35 18 9 32 op rs rt 16 bit number
Where's the compromise?

## Slide 14: Formatos de instrução já vistos

## Slide 15: Exemplo (pag 119)
C code: A[300] = h + A[300];
MIPS code: lw $t0, 1200($t1)
add $t0, $s2, $t0 sw $t0, 1200($t1)

## Slide 16: Instruções vistas até agora

## Slide 17: Stored Program Concept
Instructions are bits
Programs are stored in memory — to be read or written just like data
Fetch & Execute Cycle
  Instructions are fetched and put into a special register
  Bits in the register "control" the subsequent actions
  Fetch the “next” instruction and continue
Processor
Memory
memory for data, programs,
compilers, editors, etc.

## Slide 18: Control (3.5)
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions: bne $t0, $t1, Label beq $t0, $t1, Label

## Slide 19: Example (pag 123)
(assumir f g h i j  $s0 -> $s4) if (i = = j) goto L1; f = g + h; L1: f = f - i; beq $s3, $s4, Label # goto label if i  j add $s0, $s1, $s2 # faz a soma Label: sub $s0, $s0, s$3
e se não há label explícito no código C? if (i != j) f = g + h; f = f - i; assembler cria label

## Slide 20: Control
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...
Can you build a simple for loop? for (i=0; i < n; i = i + 1) i <- 0 label: corpo do for i = i + 1 teste (usando beq ou bne)-> label

## Slide 21: So far:
Instruction Meaning add $s1,$s2,$s3 $s1 = $s2 + $s3 sub $s1,$s2,$s3 $s1 = $s2 – $s3 lw $s1,100($s2) $s1 = Memory[$s2+100] sw $s1,100($s2) Memory[$s2+100] = $s1 bne $s4,$s5,L Next instr. is at Label if $s4 ° $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 22: Control Flow (if then else)
if (i == j) f = g + h ; else f = g - h;
$s3 $s4 $s0 $s1 $s2
bne $s3, $s4, Else # goto Else if i  j
add $s0, $s1, $s2 # f = g + h
j Exit
Else: sub $s0, $s1, $s2 # f = g - h
Exit: ....
Notes: Board work: Binary Numbers

## Slide 23: Control Flow (slt)
slt (set-on-less-than): if $s1 < $s2 then $t0 = 1 slt $t0, $s1, $s2 else $t0 = 0
Can use this instruction to build "blt $s1, $s2, Label" — can now build general control structures
Note that the assembler needs a register to do this, — there are policy of use conventions for registers

## Slide 24: Policy of Use Conventions
$1 = $at: reservado para o assembler
$26-27 = $k0-$k1: reservados para o sistema operacional

## Slide 25: Uso do $zero
Zero é um valor útil
Custo em hardware é (quase) nulo
Útil, por exemplo, para implementar
  mov $s1, $s2 # $s1  $s2
  clear $s1 # $s1  0
  blt $s1, $s2, Label # branch on less than

## Slide 26: Exemplo: loop com array (pag 126)
Loop: g = g + A[i]; # (g h i j A)
i = i + j; # ($s1 $s2 $s3 $s4 $s5)
if (i != h) goto Loop;
Loop: add $t1, $s3, $zero # $t1  i
multi $t1, $t1, 4 # $t1  i * 4 (instrução adiante)
add $t1, $t1, $s5 # $t1  i * 4 + A (posição do elemento)
lw $t0, 0($t1) # $t0  A[i]
add $s1, $s1, $t0 # g  g + A[i]
add $s3, $s3, $s4 # i = i + j
bne $s3, $s2, Loop # goto Loop if i  h

## Slide 27: Exemplo: while loop (pag 127)
Loop: while (save[i] = = k) # (i j k save)
i = i + j; # ($s3 $s4 $s5 $s6)
Loop: add $t1, $s3, $zero # $t1  i
multi $t1, $t1, 4 # $t1  i * 4 (instrução adiante)
add $t1, $t1, $s6 # $t1  i * 4 + save
lw $t0, 0($t1) # $t0  save[i]
bne $t0, $s5, Exit # goto Exit if save[i]  k
add $s3, $s3, $s4 # i = i + j
j Loop
Exit: ....
(ver exercício 3.9 para otimização, reduzindo para uma instrução de desvio por ciclo)

## Slide 28: Case / switch e jr (pag 129)
switch (k) { # (f g h i j k)
case 0: f=i+j; break; # ($s0 $s1 $s2 $s3 $s4 $s5)
case 1: f=g+h; break; # ($t2 contém o valor 4)
case 2: f=g-h; break; # ($t4 contém base de JumpTable)
case 3: f=i-j; break;
}
(testar primeiro se k dentro de 0-3)
add $t1, $s5, $zero # $t1  k
multi $t1, $t1, 4 # $t1  i * 4
add $t1, $t1, $t4 # $t1  k * 4 + JumpTable
lw $t0, 0($t1) # $t0  endereço a ser saltado
jr $t0 # salta para o endereço
...
L0: add $s0, $s3, $s4 # f = i + j
j Exit # break
L1: add $s0, $s1, $s2 # f = g + h
j Exit # break
...
ifs aninhados?
quem é melhor?

## Slide 29: Chamada de procedimentos
Desvio: passar parâmetros, executar (salvar contexto), retornar, (recuperar contexto)
Instrução SIMPLES do MIPS  jal endereço
  desvia para endereço
  salva “automaticamente” endereço da próxima instrução em $ra ($31)
O que acontece com jal aninhados?
Solução: pilha
  MIPS: implementada na memória, com $sp ($29)
  ver exemplos pag 134 - 139
push $ra
addi $sp, $sp, -4 sw $ra, 0($sp)
pop $ra
lw $ra, 0($sp) addi $sp, $sp, 4

## Slide 30: Chamada de procedimentos
contexto:
  endereço de retorno
  registradores tipo $sn (devem ser salvos, não podem ser alterados)
salvamento do contexto
  pelo “caller”
  pelo “callee”
argumentos passados entre o chamador e o chamado
  usar os registradores $a0 = $a3
temporários não precisam ser salvos

## Slide 31: Constants
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
Solutions? Why not?
  put 'typical constants' in memory and load them.
  create hard-wired registers (like $zero) for constants like one.
MIPS Instructions: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4
How do we make this work?

## Slide 32: How about larger constants?
We'd like to be able to load a 32 bit constant into a register
Must use two instructions, new "load upper immediate" instruction lui $t0, 1010101010101010
Then must get the lower order bits right, i.e., ori $t0, $t0, 1010101010101010
1010101010101010
0000000000000000
0000000000000000
1010101010101010
1010101010101010
1010101010101010
ori
1010101010101010
0000000000000000
filled with zeros

## Slide 33: Assembly Language vs. Machine Language
Assembly provides convenient symbolic representation
  much easier than writing down numbers
  e.g., destination first
Machine language is the underlying reality
  e.g., destination is no longer first
Assembly can provide 'pseudoinstructions'
  e.g., “move $t0, $t1” exists only in Assembly
  would be implemented using “add $t0,$t1,$zero”
When considering performance you should count real instructions

## Slide 34: Other Issues
Things we are not going to cover linkers, loaders, memory layout stacks, frames, recursion manipulating strings and pointers interrupts and exceptions system calls and conventions
Some of these we'll talk about later
We've focused on architectural issues
  basics of MIPS assembly language and machine code
  we’ll build a processor to execute these instructions.

## Slide 35: Overview of MIPS
simple instructions all 32 bits wide
very structured, no unnecessary baggage
only three instruction formats
rely on compiler to achieve performance — what are the compiler's goals?
help compiler where we can
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 36: Addresses in Branches and Jumps
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4  $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
  j Label Next instruction is at Label
Formats:
Addresses are not 32 bits — How do we handle this with load and store instructions?
op rs rt 16 bit address
op 26 bit address
I
J

## Slide 37: Addresses in Branches
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4 $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
Formats:
Could specify a register (like lw and sw) and add it to address
  use Instruction Address Register (PC = program counter)
  most branches are local (principle of locality)
Jump instructions just use high order bits of PC
  address boundaries of 256 MB
op rs rt 16 bit address
I

## Slide 38: To summarize:

## Slide 40: Alternative Architectures
Design alternative:
  provide more powerful operations
  goal is to reduce number of instructions executed
  danger is a slower cycle time and/or a higher CPI
Sometimes referred to as “RISC vs. CISC”
  virtually all new instruction sets since 1982 have been RISC
  VAX: minimize code size, make assembly language easy instructions from 1 to 54 bytes long!
We’ll look at PowerPC and 80x86

## Slide 41: Um exemplo completo
mostrar transparência do sort
  para ilustrar estrutura geral
  não será cobrado
array e pointer
  não será cobrado

## Slide 42: PowerPC (Motorola, Apple, IBM)
32 registradores de 32 bits, instruções de 32 bits
Indexed addressing
  example: lw $t1,$a0+$s3 #$t1=Memory[$a0+$s3]
  What do we have to do in MIPS?
Update addressing
  update a register as part of load (for marching through arrays)
  example: lwu $t0,4($s3) #$t0=Memory[$s3+4];$s3=$s3+4
  What do we have to do in MIPS?
Others:
  load multiple/store multiple
  a special counter register “bc Loop” decrement counter, if not 0 goto loop

## Slide 43: 80x86
1978: The Intel 8086 is announced (16 bit architecture)
1980: The 8087 floating point coprocessor is added
1982: The 80286 increases address space to 24 bits, +instructions
1985: The 80386 extends to 32 bits, new addressing modes
1989-1995: The 80486, Pentium, Pentium Pro add a few instructions (mostly designed for higher performance)
1997: MMX is added “This history illustrates the impact of the “golden handcuffs” of compatibility “adding new features as someone might add clothing to a packed bag” “an architecture that is difficult to explain and impossible to love”

## Slide 44: A dominant architecture: 80x86
See your textbook for a more detailed description
Complexity:
  Instructions from 1 to 17 bytes long
  one operand must act as both a source and destination
  one operand can come from memory
  complex addressing modes e.g., “base or scaled index with 8 or 32 bit displacement”
Saving grace:
  the most frequently used instructions are not too difficult to build
  compilers avoid the portions of the architecture that are slow
“what the 80x86 lacks in style is made up in quantity, making it beautiful from the right perspective”

## Slide 45: Conclusão
Erro: instruções mais poderosas aumentam desempenho
VAX:
  CALL: salva endereço de retorno, nº de parâmetros, quaisquer registros modificados e valor antigo do SP
  instrução para apagar lista duplamente ligada
IBM 360:
  10 instruções mais freqüentes: 80% das ocorrências
  16 instruções mais freqüentes: 90% das ocorrências
  21 instruções mais freqüentes: 95% das ocorrências
  30 instruções mais freqüentes: 99% das ocorrências
MIPS

## Slide 46: Summary
Instruction complexity is only one variable
  lower instruction count vs. higher CPI / lower clock rate
Design Principles:
  simplicity favors regularity (facilidade de projeto)
  smaller is faster
  good design demands compromise
  make the common case fast (RISC)
Instruction set architecture
  a very important abstraction indeed!

## Slide 47: Máquinas de 0, 1, 2 e 3 endereços
X = A * B + C * C onde X, A, B, C são endereços de posições de memória
MOVE T, A
MULTIPLY T, B
MOVE X, C
MULTIPLY X, C
ADD X, T
END1  END1 op END2
Dois endereços
LOAD A
MULTIPLY B
STORE T
LOAD C
MULTIPLY C
ADD T
STORE X
Um endereço
AC  AC op END
MULTIPLY T, A, B MULTIPLY X, C, C
ADD X, X, T
END1  END2 op END3
Três endereços
push A
push B
mult
push C
push C
mult
add
pop X
tos  tos op tos
Zero endereços
load R1, A
load R2, B
load R3, C
mult R1, R1, R2
mult R3, R3, R3
add R1, R1, R3
store R1, X
R1  R2 op R3
Load-Store

## Slide 48: Máquinas de 0, 1, 2 e 3 endereços
Qual é o melhor?
  tamanho do código fonte
  tamanho do código objeto
  tempo de execução
  simplicidade e desempenho do hardware para suportar arquitetura