## Slide 1: Chapter Four Arithmetic for Computers

## Slide 2: Arithmetic
Where we've been:
  Performance (seconds, cycles, instructions)
  Abstractions: Instruction Set Architecture Assembly Language and Machine Language
What's up ahead:
  Implementing the Architecture
32
32
32
operation
result
a
b
ALU

## Slide 3: Numbers
Bits are just bits (no inherent meaning) — conventions define relationship between bits and numbers
Binary numbers (base 2) 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001... decimal: 0...2n-1
Of course it gets more complicated: numbers are finite (overflow) fractions and real numbers negative numbers e.g., no MIPS subi instruction; addi can add a negative number)
How do we represent negative numbers? i.e., which bit patterns will represent which numbers?

## Slide 4: Possible Representations
Sign Magnitude: One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: balance, number of zeros, ease of operations
Which one is best? Why?

## Slide 5: MIPS
32 bit signed numbers: 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten 0000 0000 0000 0000 0000 0000 0000 0010two = + 2ten ... 0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0010two = – 2,147,483,646ten ... 1111 1111 1111 1111 1111 1111 1111 1101two = – 3ten 1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint

## Slide 6: Two's Complement Operations
Negating a two's complement number: invert all bits and add 1
  remember: “negate” and “invert” are quite different!
Converting n bit numbers into numbers with more than n bits:
  MIPS 16 bit immediate gets converted to 32 bits for arithmetic
  copy the most significant bit (the sign bit) into the other bits 0010 -> 0000 0010 1010 -> 1111 1010
  "sign extension" (lbu vs. lb)

## Slide 7: Novas instruções
instruções “unsigned”: (exemplo de aplicação, cálculo de memória)
sltu $t1, $t2, $t3 # diferença é “sem sinal”
slti e sltiu # envolve imediato, com ou sem sinal
Exemplo pag 215: supor $s0 = FF FF FF FF e $s1 = 00 00 00 01
slt $t0, $s0, $s1
como $s0 < 0 e $s1 > 0  $s0<$s1  $t0 = 1
sltu $t0, $s0, $s1
como $s0 e $s1 não tem sinal  $s0>$s1  $t0 = 0

## Slide 8: Cuidados com extensão 16 bits
beq $s0, $s1, nnn # salta para PC + nnn se teste OK
nnn tem 16 bits e PC tem 32 bits
  estender de 16 para 32 bits antes daoperação aritmética
se nnn > 0
  preencher com zeros à esquerda
se nnn < 0 CUIDADO
  preencher com 1´s à esquerda
  verificar
por este motivo operação é chamada de
  EXTENSÃO DE SINAL

## Slide 9: Addition & Subtraction
Just like in grade school (carry/borrow 1s) 0111 0111 0110 + 0110 - 0110 - 0101
Two's complement operations easy
  subtraction using addition of negative numbers 0111 + 1010
Overflow (result too large for finite computer word):
  e.g., adding two n-bit numbers does not yield an n-bit number 0111 + 0001 note that overflow term is somewhat misleading, 1000 it does not mean a carry “overflowed”

## Slide 10: Detecting Overflow
No overflow when adding a positive and a negative number
No overflow when signs are the same for subtraction
CONDIÇÕES DE OVERFLOW
Em hardware, comparar o “vai-um” e o
“vem-um” com relação ao bit de sinal

## Slide 11: Effects of Overflow
An exception (interrupt) occurs
  Control jumps to predefined address for exception (EPC — EXCEPTION PROGRAM COUNTER)
  Interrupted address is saved for possible resumption
    mfc0 (move from system control): copia endereço do EPC para qualquer registrador
Don't always want to detect overflow — new MIPS instructions: addu, addiu, subu note: addiu still sign-extends! note: sltu, sltiu for unsigned comparisons

## Slide 12: Instruções (fig 4.52 - pag 309)

## Slide 13: Review: Boolean Algebra & Gates
Problem: Consider a logic function with three inputs: A, B, and C. Output D is true if at least one input is true Output E is true if exactly two inputs are true Output F is true only if all three inputs are true
Show the truth table for these three functions.
Show the Boolean equations for these three functions.
Show an implementation consisting of inverters, AND, and OR gates.

## Slide 14: An ALU (arithmetic logic unit)
Let's build an ALU to support the andi and ori instructions
  we'll just build a 1 bit ALU, and use 32 of them
Possible Implementation (sum-of-products):
b
a
operation
result
op
a
b
res

## Slide 15: Review: The Multiplexor
Selects one of the inputs to be the output, based on a control input
Lets build our ALU using a MUX:
S
C
A
B
0
1
note: we call this a 2-input mux
even though it has 3 inputs!

## Slide 16: Different Implementations
Not easy to decide the “best” way to build something
  Don't want too many inputs to a single gate
  Dont want to have to go through too many gates
  for our purposes, ease of comprehension is important
Let's look at a 1-bit ALU for addition:
How could we build a 1-bit ALU for add, and, and or?
How could we build a 32-bit ALU?
cout = a b + a cin + b cin
sum = a xor b xor cin

## Slide 17: Building a 32 bit ALU

## Slide 18: What about subtraction (a – b) ?
Two's complement approch: just negate b and add.
a - b = a + (- b)
How do we negate?
(- a) = comp2(a) = comp1(a) + 1
A very clever solution:

## Slide 19: Subtrator
0 1
Binv
B
~B
equivalente à

B
Binv
Binv
+

+

+

+


## Slide 20: Tailoring the ALU to the MIPS
Need to support the set-on-less-than instruction (slt)
  remember: slt is an arithmetic instruction
  produces a 1 if rs < rt and 0 otherwise
  use subtraction: (a-b) < 0 implies a < b
Need to support test for equality (beq $t5, $t6, $t7)
  use subtraction: (a-b) = 0 implies a = b

## Slide 21: Supporting slt
Can we figure out the idea?
0
Rs
Rt
Rd
bit de sinal
subtração

## Slide 23: Test for equality
Notice control lines: 000 = and 001 = or 010 = add 110 = subtract 111 = slt
Note: zero is a 1 when the result is zero!

## Slide 24: ALU
Overflow
ALUop
A
B
Zero
Result
32 bits: A, B, result
1 bit: Zero, Overflow
3 bits: ALUop

## Slide 25: Conclusion
We can build an ALU to support the MIPS instruction set
  key idea: use multiplexor to select the output we want
  we can efficiently perform subtraction using two’s complement
  we can replicate a 1-bit ALU to produce a 32-bit ALU
Important points about hardware
  all of the gates are always working
  the speed of a gate is affected by the number of inputs to the gate
  the speed of a circuit is affected by the number of gates in series (on the “critical path” or the “deepest level of logic”)
Our primary focus: comprehension, however,
  Clever changes to organization can improve performance (similar to using better algorithms in software)
  we’ll look at two examples for addition and multiplication

## Slide 26: Problem: ripple carry adder is slow
Is a 32-bit ALU as fast as a 1-bit ALU? atraso (ent  soma ou carry = 2G) n estágios 2nG
Is there more than one way to do addition?
  two extremes: ripple carry (2nG) sum-of-products (2G)
Can you see the ripple? How could you get rid of it?
c1 = b0c0 + a0c0 + a0b0
c2 = b1c1 + a1c1 + a1b1 c2 =
c3 = b2c2 + a2c2 + a2b2 c3 =
c4 = b3c3 + a3c3 + a3b3 c4 =
Not feasible! Why?

## Slide 27: Carry-lookahead adder
An approach in-between our two extremes
Motivation:
  If we didn't know the value of carry-in, what could we do?
  When would we always generate a carry? gi = ai bi
  When would we propagate the carry? pi = ai + bi
Did we get rid of the ripple?
c1 = g0 + p0c0
c2 = g1 + p1c1 c2 =
c3 = g2 + p2c2 c3 =
c4 = g3 + p3c3 c4 = Feasible! Why?
atraso: ent  gi pi (1G) gi pi  carry (2G) carry  saídas (2G)
total: 5G independente de n

## Slide 28: Use principle to build bigger adders
Can’t build a 16 bit adder this way... (too big)
Could use ripple carry of 4-bit CLA adders
Better: use the CLA principle again!
  super propagate (ver pag 243)
  super generate (ver pag 245)
  ver exercícios 4.44, 45 e 46 (não será cobrado)

## Slide 29: Multiplication
More complicated than addition
  accomplished via shifting and addition
More time and more area
Let's look at 3 versions based on gradeschool algorithm
Negative numbers: convert and multiply
  there are better techniques, we won’t look at them

## Slide 30: Multiplication: Implementation

## Slide 31: Second Version

## Slide 32: Final Version
No MIPS:
  dois novos registradores de uso dedicado para multiplicação: Hi e Lo (32 bits cada)
  mult $t1, $t2 # Hi Lo  $t1 * $t2
  mfhi $t1 # $t1  Hi
  mflo $t1 # $t1  Lo

## Slide 33: Algoritmo de Booth (visão geral)
Idéia: “acelerar” multiplicação no caso de cadeia de “1´s” no multiplicador:
  0 1 1 1 0 * (multiplicando) =
  + 1 0 0 0 0 * (multiplicando)
  - 0 0 0 1 0 * (multiplicando)
Olhando bits do multiplicador 2 a 2
  00 nada
  01 soma (final)
  10 subtrai (começo)
  11 nada (meio da cadeia de uns)
Funciona também para números negativos
Para o curso: só os conceitos básicos
Algoritmo de Booth estendido
  varre os bits do multiplicador de 2 em 2
Vantagens:
  (pensava-se: shift é mais rápido do que soma)
  gera metade dos produtos parciais: metade dos ciclos

## Slide 34: Geração rápida dos produtos parciais
Y0
Y1
Y2
X2
X1
X0
X2 Y0
X2 Y1
X2 Y2
X1 Y2
X1 Y1
X1 Y0
X0 Y0
X0 Y1
X0 Y2

## Slide 35: Carry Save Adders (soma de produtos parciais)

## Slide 36: Divisão
29  3  29 = 3 * Q + R = 3 * 9 + 2
dividendo
divisor
quociente
resto
2910 = 011101 310 = 11
0 1 1 1 0 1 1 1
1 1 0 1 0 0 1
0 0 1 0 1
1 1
1 0
Q = 9 R = 2
Como implementar em hardware?

## Slide 37: Alternativa 1: divisão com restauração
q4q3q2q1q0 = 01001 = 9
R = 11 = 2
hardware não sabe se “vai caber ou não”
registrador para guardar resto parcial
verificação do sinal do resto parcial
caso negativo  restauração

## Slide 38: Alternativa 2: divisão sem restauração
Regras

## Slide 39: Alternativa 2: conversão do resultado
16 - 8 + 4 - 2 - 1
Nº de somas: 3
Nº de subtrações:2
Total: 5
OBS: se resto < 0 deve haver correção de um divisor para que resto > 0

## Slide 40: Comparação das alternativas

## Slide 41: Hardware para divisão: terceira alternativa

## Slide 42: Instruções
No MIPS:
  dois novos registradores de uso dedicado para multiplicação: Hi e Lo (32 bits cada)
  mult $t1, $t2 # Hi Lo  $t1 * $t2
  mfhi $t1 # $t1  Hi
  mflo $t1 # $t1  Lo
Para divisão:
  div $s2, $s3 # Lo  $s3 / $s3 Hi  $s3 mod $s3
  divu $s2, $s3 # idem para “unsigned”

## Slide 43: Ponto Flutuante
Objetivos:
  representação de números não inteiros
  aumentar a capacidade de representação (maiores ou menores)
Formato padronizado
  1.XXXXXXXXX ..... * 2yyy (no caso geral Byyy)
No MIPS:
S
exp
mantissa ou significando
8
23
sinal-magnitude (-1)S F * 2E
 exp  mantissa
 faixa
 precisão

## Slide 44: Ponto Flutuante e padrão IEEE 754
S
exp
mantissa ou significando
8
23
expoente  [-128 , 127] se 210  103
128 = 8 + 10 * 12;
2128 = 2(8 + 10 * 12) = 28 * 2(10 * 12)  2 * 1038
overflow  Nº > 1038
underflow  Nº < 10-38
PADRÃO IEEE 754
1.XXXXXXXXXXX
um implícito
mantissa: precisão simples: 23 bits (+1)
precisão dupla: 52 bits (+1)

## Slide 45: Padrão IEEE754: bias
Nº = (-1)S (1 + Mantissa) * 2E
Para simplificar a ordenação (sorting): BIAS
0 127 255
exp Bias exp
No padrão: 2 (nE - 1) - 1 = 127
EXP = CAMPOEXP - BIAS
Exemplo: representar - 0,7510 = - (1/2 + 1/4)
- 0,7510 = - 0,112 = -1,11 * 2-1
mantissa = 1000000 ...... (23 bits)
campo expoente: - 1 + 127 = 12610 = 0111 11102
1
0111 1110
1000 0000 0000 0000 0000 000

## Slide 46: Tabela de faixas de representação do IEEE 754

## Slide 47: Soma em ponto flutuante

## Slide 48: ULA para soma em ponto flutuante

## Slide 49: Multiplicação em ponto flutuante

## Slide 50: Conjunto de instruções do MIPS para fp
Fig 4.47 Pag 291

## Slide 51: Floating Point Complexities
Operations are somewhat more complicated (see text)
In addition to overflow we can have “underflow”
Accuracy can be a big problem
  IEEE 754 keeps two extra bits, guard and round
  four rounding modes
  positive divided by zero yields “infinity”
  zero divide by zero yields “not a number”
  other complexities
Implementing the standard can be tricky
Not using the standard can be even worse
  see text for description of 80x86 and Pentium bug!

## Slide 52: Chapter Four Summary
Computer arithmetic is constrained by limited precision
Bit patterns have no inherent meaning but standards do exist
  two’s complement
  IEEE 754 floating point
Computer instructions determine “meaning” of the bit patterns
Performance and accuracy are important so there are many complexities in real machines (i.e., algorithms and implementation).
We are ready to move on (and implement the processor) you may want to look back (Section 4.12 is great reading!)